## Slide 1
Configuring 5G Test Bed
5G Core, RAN & UE

## Slide 2
OAI-Setup
Refer to the following Documentations to configure the 5GC, RAN and UE. Run the Commands on the Terminal
  5GC - Click_Here
  NR-UE - Click Here (Use the RFsimulator for GnB and UE)

## Slide 3
Basic Troubleshooting Commands and Methods
  docker ps – Lists running OAI-CN5G containers to verify active components
  ifconfig – Shows network interfaces and IP addresses for connectivity checks
  docker logs <container-name> – Displays logs from containers for debugging and monitoring

## Slide 4
Testing IF UE is succesfully Registered
Method 1 - Check AMF Logs:
  Use command: docker logs oai-amf
Logs like this Indicate that the UE is registerd to the 5GC
FIG 1. AMF LOGS

## Slide 5
Testing IF UE is succesfully Registered
Method 2 - Ping from UE to External Data Network:
  Use command: ping -I oaitun_ue1 -c 4 192.168.70.135
Logs like this Indicate that the UE Can successfully ping ext-dn
FIG 2. PINGING EXT-DN

## Slide 6
Testing IF UE is succesfully Registered
Method 3 - Use Wireshark:
  We can use Wireshark to monitor the packets being sent and view when the UE-tunnel is being established.

## Slide 7
Thank You